Sentence definitions

The first two $GPGGA, $GPRMC are standard NMEA GPS output. The sentences beginning with $FH are Far Horizons sentences. and documented below. The $FH sentences begin with fields that contain data, the trailing fields are for diagnostics. Following the NMEA standard all fields are separated by commas. The uniformity allows the use of utilities such as awk to parse wanted data, and create reports.

Sentence $FHMAG - Far Horizons Magentometer

The data is from Modified 5883L.h Library. The int declarations where chaged from int to int16_t in the header file.

count
heading in degrees
heading in Radians
raw.XAxis
raw.YAxis
raw.ZAxis
scaled.XAxis
scaled.YAxis
scaled.ZAxis

Sentence $FHPRS Far Horizons Pressure.

The data is from code modified by Jeff to get the math correct

count
Temperature
Pressure
D2 - For diagnostics
D1 - For diagnostics
dT - For diagnostics
SENS - For diagnostics
OFF/100 - For diagnostics
T2 - For diagnostics
SENS2 - For diagnostics
 OFF2/100 - For diagnostics

 Sentence $FHACC Far Horizons Accelerometer

The code for the ADXL345 was lifted from the ADXL#$%.h example. However in the sketch, the interger valeues were cast to int16_t.

count
Axg - Scaled, 16bit x axis gravity
Ayg - Scaled, 16bit y axis gravity
Azg - Scaled, 16bit z axis gravity
Ax - Raw 32 bit x axis input
Ay - Raw 32 bit x axis input
Az - Raw 32 bit x axis input

Sample Output:

$GPGGA,160118.000,4203.2494,N,08741.2429,W,1,5,1.90,197.7,M,-34.1,M,,*66
$GPRMC,160118.000,A,4203.2494,N,08741.2429,W,0.36,261.60,020514,,,A*7E
$FHMAG,5468,161.23,2.81,-120,47,-296,-120.00,47.00,-296.00
$FHPRS,5468,22.72,989.06,8691140,5976978,82628.00,2998217472.00,53041084.00,0.00,0.00,0.00
$FHACC,5468,0.09,-0.09,0.91,3,65533,29

$GPGGA,160119.000,4203.2494,N,08741.2431,W,1,5,1.90,197.7,M,-34.1,M,,*6E
$GPRMC,160119.000,A,4203.2494,N,08741.2431,W,0.35,261.10,020514,,,A*72
$FHMAG,5469,160.82,2.81,-120,48,-297,-120.00,48.00,-297.00
$FHPRS,5469,22.72,989.13,8691196,5977128,82684.00,2998230016.00,53041312.00,0.00,0.00,0.00
$FHACC,5469,0.09,-0.09,0.88,3,65533,28

$GPGGA,160120.000,4203.2494,N,08741.2432,W,1,5,1.90,197.7,M,-34.1,M,,*67
$GPRMC,160120.000,A,4203.2494,N,08741.2432,W,0.35,262.81,020514,,,A*70
$FHMAG,5470,162.22,2.83,-121,45,-296,-121.00,45.00,-296.00
$FHPRS,5470,22.72,989.08,8691248,5977002,82736.00,2998241280.00,53041520.00,0.00,0.00,0.00
$FHACC,5470,0.09,-0.09,0.91,3,65533,29

$GPGGA,160121.000,4203.2494,N,08741.2433,W,1,5,1.90,197.7,M,-34.1,M,,*67
$GPRMC,160121.000,A,4203.2494,N,08741.2433,W,0.35,267.85,020514,,,A*71
$FHMAG,5471,161.32,2.82,-118,46,-296,-118.00,46.00,-296.00
$FHPRS,5471,22.72,989.06,8691246,5976968,82734.00,2998241024.00,53041512.00,0.00,0.00,0.00
$FHACC,5471,0.09,-0.09,0.88,3,65533,28

Sample Awk Script

The foillowing awk script:

# Records are separated by blank lines.
# Commas separate the fields.
BEGIN { RS = "" ; FS = "," }

{
      print $25, $2, $3, $4, $5, $6, $10, $11, $31, $41, $42, $53, $54, $55
      print ""
}

yields GPS Date, GPS Tine, GPS Lat, GPS Long, GPS, Alt, Magnetometer heading, Pressure Sensor Temp, Pressure Sensor Pressure, X Acceleration, Y Acceleration, Z Acceleration.

$ awk -f awk_test.awk awk_test.txt
020514 160118.000 4203.2494 N 08741.2429 W 197.7 M 161.23 22.72 989.06 0.09 -0.09 0.91

020514 160119.000 4203.2494 N 08741.2431 W 197.7 M 160.82 22.72 989.13 0.09 -0.09 0.88

020514 160120.000 4203.2494 N 08741.2432 W 197.7 M 162.22 22.72 989.08 0.09 -0.09 0.91

020514 160121.000 4203.2494 N 08741.2433 W 197.7 M 161.32 22.72 989.06 0.09 -0.09 0.88